## Slide 1: Machine Learning-Based Detection of Cardiovascular Diseases Presentation 2

## Slide 2: Agenda
Progress Report
Literature Review Findings
Comparison of Methodologies
Limitations
Outcome of Research
Next Steps
Challenges

## Slide 3: Progress Report (December 21-January 22)
We reviewed over 42 research papers and publications.
Extracted valuable information such as methodology, approach, limitations, and databases.
We took a Data-driven approach towards our Project and applied our learned information to the Data Preprocessing and Model Training Steps.
We have successfully Preprocessed data and started testing different DL and ML models.

## Slide 4: Literature Review and Findings
From the 42 studies, publications, and research complied CNN is dominantly observed as the suitable technique for training a machine learning model for reading ECGs.
About 52% of studies employed a CNN model or a variation of a CNN model such as AB-CNN, CNN-LSTM, etc. to detect irregularities in the ECG signal.
ECG signals are low-frequency and weak electrical signals that are extremely vulnerable to the influence of external noise.
Therefore, one of the biggest challenges is not training the model , but denoising the ECG signal and getting accurate data.

## Slide 5: Literature Review and Findings
ECG interference can be classified into three main categories: industrial frequency, electromyographic interference, and baseline drift.
To denoise the ECG signal, Wavelet Transform has been used in all of the publications studied, coupled with other methods such as GAN (Generative Adversarial Network)
Wavelet Transform has been heavily used and deemed more efficient than Fourier Transform in those studies.

## Slide 6: Comparison of Methodologies
Publication | Dataset | Method | Accuracy | Limitation
Yan, Zhang, 2021 | MIT-BIH ECG Dataset | Denoised the ECG signals using WT. Extracted features and fed into SVM. | Classified six classes of ECG signals with 96.3% accuracy. | Computationally Expensive and slow compared to other methods
Mehmet et al., 2021 | MIT-BIH ECG Dataset, PTB ECG Dataset, INCART dataset | Multi-level features were generated using HIT pattern and MAP decomposer and then fed into SVM to classify chose | Attained 92.95% and 97.18% accuracy for seven- and four- class arrythmia classification, respectively. | Although it’s computationally lightweight with a low time burden, it has low accuracy.
Wu et al., 2021 | MIT-BIH ECG Dataset | Denoised the ECG signals using WT and then fed it into CNN. | Attained 97.41% accuracy | 
Albadvi et al., 2021 | MIT-BIH ECG Dataset | FIR band-pass filter to filter and eliminate noise from QRS complex of ECG signals. Multiclass Random Forest model was developed and data was streamed in real time. | Attained 88.6% accuracy and average consumption time of 1 second. Only detected 3 types of cardiac arrhythmia. | Very low accuracy, computational expensive, and not as effective in denoising.

## Slide 7: Comparison of Methodologies - Continued
Publication | Dataset | Method | Accuracy | Limitation
Liu, Zhang, 2021 | MIT-BIH ECG Dataset, PTB ECG Dataset, INCART Dataset | WT to denoise ECG signal. Then ABCNN was used to assign higher weight to more informative signals. Attention was directed towards QRS complex. | AUC of 98.96% and accuracy of 96%. | Computationally Expensive, and performs slower than other models mentioned.
Siddique et al., 2021 | MIT-BIH ECG Dataset, PTB ECG Dataset | WT to denoise ECG signal. CNN + LSTM + Attentional Model was used including GAN to create new data instances that resemble training data. | 99.12% for CNN model, 99.3% for CNN + LTSM model, 99.29% for CNN + LTSM model + Attentional model. | Creation of data using GAN can be questionable because they aren’t real.
Pandey et al., 2021 | MIT-BIH ECG Dataset, PTB ECG Dataset, INCART Dataset | Signal processing by Normalizing heart beats, then segmenting the heart beats. Using a Stacked RBM model to extract features from ECG signals, and then SoftMAx activation function to classify four types of heartbeats. | Overall accuracy of 98.61% with sensitivity of 89.07% and specificity of 98.93%. | Training the RBM model is difficult and computationally expensive.

## Slide 8: Limitations
High accuracy was obtained by overfitting or only filtering out the QRS complex.
Size of Dataset is small, which is why accuracy is so high
Most proposed models are computationally intensive with huge memory footprint (at least 16 GB RAM is required to train the data)
Proposed DL methods are effective for limited number of Arrhythmia classes (three to six classes)
Publications were heavily focused on ECG signal characteristics, and not focused on patients’ physical state

## Slide 9: Outcome of Research
After studying numerous publications and studies, we’ve decided to take a research-driven approach towards processing the signals and training our model.
Seeing how successful the CNN model was, We plan to implement an Attention-based CNN model
To denoise our data, we’ll be using wavelet transform, and other denoising methods.
We also plan to use GAN and multiple datasets to avoid overfitting and gain a larger dataset.

## Slide 10: Next Steps
After analyzing publications, we’ve decided to train a very large dataset. So, we’ve compiled 20 ECG datasets, totaling over 10,000,000 heartbeats.
So far, we’re testing various sampling rates since the ECG datasets vary in sampling frequencies. We’ve had wonderful results with 125 Hz sampling rate and 360 Hz sampling rate.
Next we’ll be using the Wavelet Transform to denoise data. And Fed into a ABCNN Model.
Everything is still in testing phase and a trained model will be prepared by the next presentation.

## Slide 11: Challenges
Our challenges are finding a less computationally intensive model that is mobile-friendly.
ECG scans in Pakistan vary, so we need to train a model that closely aligns with Local ECG sampling rates and environmental noise.
Although we’ll achieve high accuracy, we need to make sure we have enough data to avoid overfitting.
We need to find an ideal sampling rate to combine all of our datasets and extract valuable information.

## Slide 12: The End
Thank You.